## Slide 1
BY: Gilad Apelstein & Etgar Daniely
ADVISOR: Dr. Shaul Ozeri
CARRIED OUT AT: DSP Research and Projects Lab

## Slide 2
MOTIVATION
How many bikes are stolen each year?
1,500,000
375,000
975,000
1,350,000
1,200,000
2
MOTIVATION

## Slide 3: OUR CONCEPT
Sampling
Sample battery movements and voltage level using an Analog Devices ADXL345 Accelerator and A/D.
The sampling is done every second in order to assure bike security.
The communication is done over SPI protocol.
1
Presenting Relevant Data
Data is sent over Bluetooth protocol to an Android application and is presented to the user.
Real-time information on battery charging level is presented and updated every second.
Our concept senses suspicious movement on the battery and notifies the user in case of theft.
3
Creating a Bluetooth Connection
Create a Bluetooth connection using HC-05 Bluetooth Module.
As soon as the user enables Bluetooth connection, the pairing is done automatically.
The relevant data is processed and is sent to the user.
The communication with the Bluetooth module is done over USART protocol.
2

## Slide 4
OUR PART
Designing a full functional circuit from scratch
Choosing components frequency-wise & voltage-wise (3.3V-5V).
Embedded software development on PIC16F1782 microprocessor.
Building the project in C in MPLABX IDE.
ADXL345 Accelerometer Integration
Synchronous master & slave Communication.
3-Wire SPI.
Clock frequency – 1.25 Mhz.
Frame size – 8 bits.
Full sense resolution of ±16g.
Measuring 3-axis differences over time.
HC-05 BT Module Integration
Bluetooth server/client communication with Android.
Async USART communication with microprocessor.
Bluetooth transmission UHF radio waves at 2.4GHz.
Full functional range up to 10 meters.
9600 baud rate 9.6 kHz.
Building an Android application
Back-end development in Java in Android Studio IDE.
Designing 4 different screens.
Client side Android Bluetooth support.
Creating a test environment and a production environment.

## Slide 5
MEETING THE EXPECTATIONS
Lorem ipsum dolor sit
amet nec at adipiscing
risus at dolor porta
3
Lorem ipsum dolor sit amet nec at adipiscing
EXPECTED
DONE
TASK
1
Building an USART communication with the HC-05 Bluetooth module
3
Integrating both modules with the PIC16F1782 Microprocessor
2
Building a SPI communication with the ADXL345 accelerometer
4
Building an Android application with Bluetooth support

## Slide 6
FURTHER SUGGESTIONS
Integrate GPS in order to know the exact battery position
Support iOS based systems
Add security & anti malware features
Cooperate with manufacturers in order to make our solution a built-in feature for future batteries
Integrate a cellular network support for a larger reception range
INTERESTING FACT: Size can get down to .
INTERESTING FACT II: Total manufacturing cost – 7$.

## Slide 7: THANKS!
Any questions?
You can find us at
ethgar.daniely@gmail.com
giladap89@gmail.com